Servo command-response protocol
All command messages must be terminated with a two-byte CRC code followed by ETX {0x03}. All controller response messages are terminated with a two-byte CRC code followed by ETX. Except as a terminating character, and possibly as a byte in the CRC code, ETX may not appear in any message.

Command format details
Messages may contain multiple commands, separated by whitespace (spaces, tabs, new lines, or carriage returns).
[n] indicates that a whole number is expected.
[d] indicates that a decimal number is expected. A whole number is acceptable. Any digits provided beyond the expected precision are ignored. For example, "3", "-4.7", and "134.00" are all acceptable decimal inputs.

Response format details
In controller report templates, '#' represents a numeric digit, '.', a decimal point, '-', a negative symbol. Other template symbols represent characters that may be non-numeric. When a reported number is positive, the negative symbol is replaced with a space, so the message length remains fixed.

Command	Description
r	Request a status report.

Response format template
"##### ##### ##### #####" (23 bytes + "\r\n")

The values represented by the symbols in the template above are, in sequence:
Command/setpoint (the commanded movement, in position units)
Position (how far the servo has moved since the beginning of the current movement)
Control output (motor drive power level)
Error (sum of active codes from the following list)
0	No error
1	ADC out of range
2	RS232 input buffer overflow
4	RS232 CRC error
8	unrecognized command from RS232
16	invalid device channel
32	datalogging time interval out of range (0..255)
64	invalid position commanded

r[n]	Start datalogging, or stop, if n is 0. Issue a controller status report every n/8 seconds. [0..255]
(e.g., "r1" means report 8 times per second)

g[n]	Move the servo n position units. [0..255] A position unit is 3.75 degrees; 96 positions is one full turn.

s	Stop any movement.
c	Stop any movement. Clear

h	Show a report header.

Response
"--Cmd --Pos --CO Error" (23 bytes + "\r\n")
z	Show program data.

Response format template
"Aeon Laboratories Servo V.########-####" (39 bytes + "\r\n")

The # symbols represent the servo firmware version.